## Slide 1: Deep Learning Assignment: Ai in Plasma
MSc in Artificial Intelligence
Eneri boniakou
NCSR-D

## Slide 2
The plasma etching process
Pattern transfer
Plasma reactor
[video]
Etching mask
plasmas are used in 35–45% of the steps in microchip manufacturing
sheath
sheath
sheath
sheath
bulk
inlet
outlet
[www.phietch.com]

## Slide 3
Physics Based Modeling
  Develop the kinetics
    reaction sets for O2/Ar chemistry
      O2 gas: 156 reactions, 13 species
      Ar gas: 40 reactions, 4 species
      Search the literature for electron impact cross sections and rate constants
    Utilize a global model for the evaluation of the reaction sets (πlasma-R code, www.plasma-r.com)
J T Gudmundsson and E G Thorsteinsson, Plasma Sources Sci. Technol. 16 399 (2007).
J. T. Gudmundsson and A. Proto, Plasma Sources Sci. Technol. 28, 045012 (2019). S. Mouchtouris and G. Kokkoris, Plasma Sources Sci. Technol. 25, 025007 (2016).
O2(b1Sg), O2(Hz), O3-, O3+

## Slide 4
Physics Based Modeling
    Develop the kinetics
      Surface (etching) kinetics
  Ion enhanced etching
G. Memos, E. Lidorikis, E. Gogolides and G. Kokkoris, Journal of Physics D: Applied Physics 2021, 54 (17)
  θο: ratio of adsorption sites occupied by O over total sites
  : fluxes of ions and neutrals
  square root of mean ion energy
  : angle of incidence
  : fitting parameter
*In this version f(ω) = 1 (no angle dependence)

## Slide 5
Physics Based Modeling
  FLUID MODEL
  Mass balances for heavy species and electrons, energy balance for electrons, momentum balance, Maxwell’s equations
GEC Reactor
2D axisymmetric geometry
    Develop the detailed 2D reactor scale model
Reactor scale model
Coil Power, pressure
Spatial distribution of densities
Electron Temperature and Ion mean energy
Etching rate
Outlet Densities
Numerical Solution: COMSOL Multiphysics

## Slide 6
Physics Based Modeling
AI Modeling
  Antenna
Instead of solving PDEs we utilize a neural network
Coil Power, pressure
Local etching rate along the wafer
Physics Based Model

## Slide 7
AI Modeling
  Train a feedforward neural network using the data acquired from the physics based model
  The neural network is a multi-layer perceptron (MLP)
  A single perceptron:
  Inputs
  Weight
  Bias
  Non – linearity/ activation function
  node
  = y
  z
  What we mean by “training” ? In simple words finding the best w matrix that minimizes the loss ground truth and the neural network prediction
m = # outputs
n = # inputs
J(W) or L(W)
  Coil Power, Pressure

## Slide 8
AI Modeling
  Power, Pressure, Etching Rates on 10 points along the wafer
4000 data points (normalized)
60% of data for training
20% of data for validation
20% of data for testing
train the NN
Iteratively run the 2D reactor scale model
Reactor scale model
 | Power (Watts) | Pump Pressure (Torr)
O2 Model | 500-2000 | 0.02-0.07
Ar Model | 50-500 | 0.01-0.06

## Slide 9
3D Plots of the data – Inputs versus the first output (the etching rate at the center of the PMMA substrate)

## Slide 10
AI Modeling
  Neural Network hyperparameter tuning
  Batch size (number of training examples used for one update of weights)
  Learning rate (how much the model updates the weights)
  Neurons per layer (adjust model’s capacity)
  Weight decay (penalty to prevent overfitting)
  To ensure generalization:
  Early stopping
  Weight decay
  Loss function:
  Weighted mean squared error

## Slide 11
AI Modeling
  Baseline
  A simple linear regression !

## Slide 12
AI Modeling
  Results – MLP (Of course on the test dataset)
Metric | M1 (O2 model) | M2 (Ar model)
Average MAE | 2.62×10-2 | 3.43×10-5
Average R2 | 0.4726 | 0.8629
  The etching rates of the O2 plasma (M1) are harder to predict than the Ar plasma (M2)…

## Slide 13
AI Modeling
  Results – MLP vs Baseline
In both models it can be seen that the NN outperforms the simple linear regression…

## Slide 14
AI Modeling
  Results – MLP vs Baseline vs SVR
O2 plasma – average SVR R2 = -4.38
Ar plasma – average SVR R2 = -0.861

## Slide 15
AI Modeling
Implement Kolmogorov – Arnold Networks (KANS)
Metric | M1 (O2 model) | M2 (Ar model)
Average MAE | 0.00418 | 0.00055
Average R2 | 0.77667 | 0.9844
KANs are still function approximators, and our experiments show that they may not learn the true underlying function, but rather an incorrect alternative…
    The trained KANs performed comparably to the MLPs but and required a more intensive training regime.

## Slide 16
AI Modeling
Implement Kolmogorov – Arnold Networks (KANS)

## Slide 17
AI Modeling
Transfer Learning
A series of experiments were performed, including:
fine-tuning the NN from the first dataset to the second and vice versa
explore catastrophic forgetting
freezing layers
investigate training with a reduced amount of data
Note on nomenclature:
M1: O2 Neural Network
M2: Ar Neural Network
D1: O2 Dataset
D2: Ar Dataset
M12: M1 trained on D2
M21: M2 trained on D1
Evaluate the model using the opposite test set, as expected poor results:

## Slide 18
AI Modeling
Transfer Learning
fine-tuning the NN from the first dataset to the second and vice versa
catastrophic forgetting

## Slide 19
freezing layers
AI Modeling
Transfer Learning
When performing the experiments it was observed that the initial layers of the NN adapt to the operating conditions of each case and its governing chemical reaction mechanism, while the deeper layers account for the solution of the PDEs and the surface mechanism, which are simulated similarly in both PBMs.

## Slide 20
AI Modeling
Transfer Learning
Since M12 performed well, we tested it by cutting down the amount of data
The metrics are calculated by evaluating the NN on the test dataset which remains the same among all experiments.
When cutting down the dataset, the distribution of data remained the same.
The data required to fine-tune the pre-trained neural network from the O2 dataset to the Ar dataset can be reduced by 50% without significantly compromising accuracy and even with less trainable parameters.

## Slide 21
Challenges
Goal: Build a pipeline that includes the development of the PBM, the training procedure of the AI model and the knowledge transfer from the pre-trained AI model on one chemistry to another
Simulation development
Data generation
Neural Network architecture and hyperparameters optimization
Exhaustive transfer learning experiments
KANs required almost 6-7 times more training time; using them in transfer learning would be hard…
I could use PINNs, but in the simulation there are solved multiple PDEs and implementing them in the loss function is not straightforward. PINNs may be useful in the future when we will use AI to predict the spatial distributions with coordinates in the reactor

## Slide 22
Thank you !